## Slide 1: FIFO
Prepared By Priyanka C Application Engineer Ramaiah Skill Academy

## Slide 2: Contents
Introduction to FIFO
Applications in VLSI design
Types of FIFO
Flags in FIFO
FIFO Architecture

## Slide 3: Introduction to FIFO
What , Why and How?

## Slide 4: What is FIFO?
First In First Out
Queue based data structure where the first item placeed into the queue is the one that is removed first.
Used especially in data management, data buffering, Clock Domain Crossing
Crucial for both hardware and software systems

## Slide 5: Why FIFO is important in VLSI?
Buffering data
Timing synchronization
Flow control
Ensuring Data Integrity
Prevention of Data Overrun and Underrun
System efficiency
Pipelining and Staging
Error Handling and Recovery

## Slide 6: FIFO In VLSI Design
Purpose: In VLSI design, FIFO is critical for transferring data between components like processors, memory blocks, and I/O interfaces. It ensures that data is not lost during high-speed data transmission or when there are different timing constraints between components.
Applications in VLSI:
  High Speed Data Transfer  Communication interfaces, network processors
  Buffering between clock domains cross clock domain data transfer(Asynchronous FIFO)
  Streaming data Applications Video processing, audio streaming, sensor data processing
  Efficient memory Utilization  by circularly allocating memory space
  Prevents overflow and underflow  by generating full flag and empty flag
  Design Flexibility

## Slide 7: Types of FIFO
Synchronous FIFO:
  Single clock pulse for both data read and write i.e., read and write operations are performed at same rate
  Depth/Words : Number of rows
  Width/ Word Length : Number of bits in each row
Asynchronous FIFO:
  Data values are written to and read from the same FIFO at different rates but at the same time.
  Used to synchronize data flow between the systems.
  Used to pass the data from one clock domain to another clock domain.

## Slide 8: Flags in FIFO
EMPTY FLAG:
  Empty flag is set when the FIFO is already empty and there is a request for a read operation.
FULL FLAG:
  Full flag is set when the FIFO is already full and there is a request for a write operation.

## Slide 9: FIFO Architecture
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Data_In
Data_Out

## Slide 10: FIFO Architecture
FIFO
Clk
Reset
Data_In
wn
rn
Data_Out
Full
Empty

## Slide 11: References
"FPGA Prototyping with Verilog examples" by Pong P. Chu
“Digital Logic Design Using Verilog” by Vaibhav Taraate

## Slide 12
Thank You