## Slide 1: Prepared By Priyanka C Application Engineer Ramaiah Skill Academy
SERIAL PERIPHERAL INTERFACE

## Slide 2: Content
Introduction to SPI protocol
Basic SPI Architecture
Working Principle
SPI Modes(Clock Polarity and Clock Phase)
Timing Diagram
Advantages of SPI
Limitations of SPI
Multi-Slave configuration
Comparison with other protocols
Applications
References

## Slide 3: Introduction to SPI
SPI is a Serial Bus communication Protocol developed by Motorola in late 1980s
It is a Synchronous, Full Duplex protocol and most used protocol for short distance communication
Used in microcontrollers, sensors, EEPROMS, ADCs, DACs etc
Has a simple hardware interface
Provides high-speed data transfer
Supports single or multiple slave devices but has only one master that controls all communications

## Slide 4: Basic SPI Architecture
Master-Slave Configuration
  One master controls the communication
  One or more slaves respond to the master
There are Four main signals:
  MOSI (Master Out Slave In)  used for sending data from Master to Slave
  MISO (Master In Slave Out)  used for sending data from Slave to Master
  SCLK (Serial Clock)  used to clock the signal
  SS/CS (Slave Select / Chip Select)  used by master to send the data by selecting a particular slave. It is used when there are multiple slaves in the design

## Slide 5: Basic SPI Architecture
MOSI
MISO
SCLK
SS/CS
MOSI
MISO
SCLK
SS/CS
SPI MASTER / CONTROLLER
SPI SLAVE / PERIPHERAL

## Slide 6: Working Principle
Clock Synchronization: where Master generates the clock SCLK
  All data transfers are synchronized to this clock.
  Data Shifts occur on clock edges determined by SPI mode.
Data Transfer
  Master sends data to the slave vis MOSI
  Slave responds with data via MISO
  Transfer happens in full duplex mode i.e., simultaneous read and write operations
Chip Selection
  SS is driven low to select a slave
  If a particular slave is not selected, it remains inactive and ignores SCLK and MOSI.
Data Frame
  SPI uses a shift register based data frame
  Data is typically transferred as 8 bits at a time but it can be extended

## Slide 7: SPI Modes ( Clock Polarity and Phase)
Mode 0 :
  CPOL = 0, CPHA = 0
  Data is sampled on rising edge
Mode 1 :
  CPOL = 0, CPHA = 1
  Data is sampled on falling edge
Mode 2 :
  CPOL = 1, CPHA = 0
  Data is sampled on falling edge
Mode 3 :
  CPOL = 1, CPHA = 1
  Data is sampled on rising edge
How to choose a mode for given hardware?

## Slide 8: Timing Diagram
Reference: www.analog.com
Start
End
Sampling edge
Shifting edge

## Slide 9: Timing Diagram
Reference: www.analog.com

## Slide 10: Timing Diagram
Reference: www.analog.com

## Slide 11: Timing Diagram
Reference: www.analog.com

## Slide 12: Advantages of SPI
High speed data transfer
Simple Implementation
Full-duplex communication
Low power consumption
Easy to daisy-chain multiple devices

## Slide 13: Limitations of SPI
No formal standard
Limited to short distances
Requires more pins than I2C
Only one master at a time
Handling multiple slaves requires extra control logic

## Slide 14: Multi-Slave Configuration
Daisy-Chain:
  Single data line for all slaves
  Advantages:
    Reduces number of SS lines
    Simple hardware connections
  Disadvantages:
    Slower due to cascading delays
    Single point of failure
Reference: www.analog.com

## Slide 15: Multi-Slave Configuration
Individual SS Lines:
  Each slave has a dedicated SS line
  Advantages:
    Faster Communication
    Better Fault Isolation
  Disadvantages:
    Requires more GPIO pins
    Complex hardware wiring for
    large systems
Reference: www.analog.com

## Slide 16: Comparison with other Protocols
Feature | SPI | I2C | UART | CAN
Speed | High | Moderate | Moderate | Low
Number of Wires | 4 (min) | 2 | 2 | 2
Full Duplex | Yes | No | No | No
Master-Slave | Single Master, Multi-Slave | Multi-Master, Multi-Slave | Point-to-Point | Multi-Master, Multi-Slave
Addressing | No | Yes | No | Yes
Robustness | Low | Medium | Medium | High
Range | Short | Short-Medium | Medium | Long

## Slide 17: Applications
Consumer Electronics:
  SD Cards, Touch screens
Industrial:
  Sensors, Actuators
Automotive:
  ECU communication

## Slide 18: Assignment
Design an SPI module in Verilog that includes both spi_master and spi_slave functionalities.
  Implement 8-bit data transfer with support for all four SPI modes (CPOL, CPHA).
  Ensure the master generates the clock (SCLK) and the slave communicates based on the Slave Select (SS) signal.
  Write a testbench to verify full-duplex communication for a given sequence of data bytes and validate correct operation through simulation waveforms.
  Explain how your design would handle scenarios where the clock speed of the SPI master is higher than the capability of the slave.

## Slide 19: References
"Serial Communication Protocols: Principles and Applications" by Robert J. Anderson, Wiley, 2020.
2. "Microcontroller Systems: Advanced Design Techniques" by John H. Davies, Elsevier, 2019.